## Slide 1: FNAL beam test results update -Zigzag GEM resolution update
A. Zhang, V. Bhopatkar, M. Phipps,
J. Twigger, M. Hohlmann
HEP Group A, Florida Tech
04/21/2014

## Slide 2
fixed Y, iterate on X
Residual sigma vs. X
track in ϕ vs. X
Residual mean vs. Y
track in ϕ vs. Y
fixed X, iterate on Y
Alignment method – (X, Y) offset
From fit on each plot, the minimal point of parabolic or 0-residual mean point can give (X, Y) offset group.

## Slide 3
Alignment method – (X, Y) and rotation
After all iterations, different quantities give different optimized (X, Y) offsets.
They are very close to lines, and have a intersect point, which is taken as the best optimized (X, Y) offset.
Then (X, Y) offsets are fixed, and the rotation of the detector is checked, from which a best rotation angle is calculated.
Line from residual sigma vs. X
Line from vs. Y

## Slide 4
Residuals after aligned
Exclusive.
σ=297±3urad
Inclusive.
σ=234±2urad
Above two residuals are for sector 4 in the middle position

## Slide 5
Resolution vs. position update
Positions in the middle sectors
Positions in the upper sectors
Previous results
Sector 7 not finished yet

## Slide 6
Resolution vs. HV with cluster size cut
Fraction of events with different cluster sizes
Resolution vs. HV
Errors smaller than markers
For the zigzag detector, most of events have cluster size 1,2 strips. At higher voltages, 3-strips events become more.
Resolution from only 2-strip events is much better: ~180μrad